SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	Central District

LOCATION		Craighten Court Tot Lot													Ward 14

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 013 |  | -too many swings | -remove two, adjust spacing |  | 1 |  |  |
| 6 Baby |  | -hanger bearings | -replace | 160 | 2 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -improper seats | -replace | 200 | 1 |  |  |
| PLG02SSM - 013 |  | -protrusions | -replace support bolts |  | 2 |  |  |
| 4 Belt |  | -hanger bearings | -replace | 160 | 2 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -encroachment | -remove swings from pines | 500 | 8 |  |  |
| PLG03HCM - 013 |  | -nil |  |  |  |  |  |
| Hand Climber |  |  |  |  |  |  |  |
| PLG04TTM - 013 |  | -too many see-saws | -remove two |  | 2 |  |  |
| Quad See-Saw |  | -cushioning | -add rubber to bottom of seats | 100 | 4 |  |  |
| PLG05SST - 013 |  | -pinch point | -re-weld |  |  |  |  |
| Int. Str. Slide |  | -entrapment | -fill and seal |  |  |  |  |
| Base Material |  | -non-sufficient safety zone | -rototill, add base material 100T |  | 8 | 1500 |  |
|  |  |  | -excavate |  | 8 | 2000 |  |
| TOTAL COST |  |  |  | 1140 | 40 | 3500 |  |

File Name: K:\PLAY\SCARB\WARD-14\CRAIGHTO.WPD