SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	West District

LOCATION 		Harding Park	         														Ward 6

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG0101SSW2536P |  | -improper spacing | -remove one swing and adjust |  |  |  | -site replacement |
| 3 Baby Swing |  | -play surface on top frame | -install cap and 1" strip |  |  |  |  |
| PLG0201JRW2536P |  | -entrapment double slide & support | -fill with plastic |  |  |  |  |
| Jr. Cr. Structure |  | -barriers | -install 32 pickets |  |  |  |  |
|  |  | -play surfaces on top rail | -install 1" strip |  |  |  |  |
|  |  | -barriers on slide | -install barriers |  |  |  |  |
|  |  | -trip hazard | -remove timber under tube crawler |  |  |  |  |
|  |  | -log chain climber | -change to rungs |  |  |  |  |
| PLG0301SRW2536P |  | -entrapment tube slide & support | -fill with plastic |  |  |  |  |
| Sr. Cr. Structure |  | -hand to hand climber | -reinstall to level |  |  |  |  |
|  |  | -tire swing attached | -remove |  |  |  |  |
|  |  | -play surface on top rail | -install 1" strip |  |  |  |  |
|  |  | -pinch points suspension bridge | -immobilize |  |  |  |  |
|  |  | -4X4 vertical ladder | -change to rungs |  |  |  |  |
| PLG04TTW2536P |  | -entrapment between supports | -remove |  |  |  |  |
| Teeter Totter |  |  |  |  |  |  |  |
| Base Material |  | -compacted | -rototill, add base material |  |  |  |  |
|  |  |  | -excavate |  |  |  |  |
| Total |  |  |  | 0 | 0 | 0 |  |

File Name: K:\PLAY\NORTH\WARD-6\HARDING