SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Longwood Park														Ward 9

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM5541P |  | -S-hooks | -replace | 10 | 1 |  |  |
| 2 Baby Swing Set |  |  |  |  |  |  |  |
| PLG02TTW5541P |  | -non sufficient safety zone |  |  |  |  |  |
| Teeter Totter |  |  |  |  |  |  |  |
| PLG03CWA5541P |  | -entanglement points all over | -remove or in fill | 100 | 3 |  |  |
| Climbing Wall |  |  |  |  |  |  |  |
| PLG05JRW5541P |  | -entrapment on steering wheel | -replace with solid wheel | 60 | 1 |  | trees over playground are dangerous |
| Jr. Cr. Structure |  | -platform requires pickets | -picket openings over 15” | 300 | 8 |  |  |
|  |  | -entrapment on the bars | -adjust the bars | 20 | 3 |  |  |
|  |  | -protrusion behind wheel | -cap | 5 | 1 |  |  |
|  |  | -entanglement at slide | -in fill | 20 | 2 |  |  |
|  |  | -no hand grip on climbing rope | -add | 100 | 2 |  |  |
|  |  | -pinch points | -remove daisy wheel |  | 1 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  |  | -add base |  |  | 600 |  |
|  |  |  | -excavate |  | 8 | 1000 |  |
| Total |  |  |  | 615 | 38 | 1600 |  |

File Name: K:\PLAY\NORTH\WARD-9\LONGWOOD