SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	North District

LOCATION		Tam O Shanter														Ward 17

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 145 |  | -improper spacing | -remove two, adjust |  | 1 |  |  |
| 4 Baby |  | -improper swings | -replace two baby swings | 120 | 1 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
| PLG02SSM - 145 |  | -improper spacing | -remove two, adjust spacing |  | 1 |  |  |
| 4 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -chipped paint | -repaint | 50 | 2 |  |  |
| PLG03INM - 145 |  | -barriers | -add pickets | 500 | 6 |  |  |
| Int. Cr. Structure |  | -slide width | -add middle rail | 400 | 3 |  |  |
|  |  | -spiral slide exit | -add exit 12” < 5º | 400 | 3 |  |  |
|  |  | -improper play area | -cap supports | 200 | 3 |  |  |
| PLG04SPR - 145 |  | -nil |  |  |  |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG05SPR - 145 |  | -nil |  |  |  |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| Base Material |  | -compacted | -rototill, add base material 44T |  | 8 | 660 |  |
|  |  | -non sufficient safety zone | -excavate |  | 8 | 1000 |  |
| Total Cost |  |  |  | 1690 | 38 | 1660 |  |

File Name: K:\PLAY\SCARB\WARD-17\OSHANTER.WPD