SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	East District

LOCATION 		Willowdale Park														Ward 10

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM4599P |  | -elevated play surface | -add 2 X 2 | 10 | 1 |  |  |
| 2 Belt 4 Baby |  | -protrusions | -cut threads |  | 1 |  |  |
| PLG02JRW4599P |  | -barriers | -picket access / egress | 50 | 4 |  |  |
| Jr. Play House |  | -entrapment | -remove tires & add rails | 50 | 4 |  |  |
|  |  | -no bar above slide | -install | 20 | 3 |  |  |
|  |  | -hand rails | -install | 40 | 4 |  |  |
|  |  | -slide edges | -remove inside edge |  | 1 |  |  |
|  |  | -bench in play surface | -remove seat |  | 1 |  |  |
|  |  | -elevated play surface | -add 2 X 2 | 12 | 2 |  |  |
| PLG03INW4599P |  | -undesignated play surface | -replace 3X6’s with 2X6’s or cut down to <2” width | 100 | 3 |  |  |
| Int. Cr. Structure |  |  |  |  |  |  |  |
| PLG05SRW4599P |  | -barriers | -picket heights >48” with proper egress access | 100 | 8 |  |  |
| Jr. Boat Structure |  | -undesignated play surface | -replace 3X6’s with 2X6’s or cut down to <2” width | 200 | 16 |  |  |
|  |  | -non sufficient safety zone | -remove spiral slide or take out part of cement pad and excavate | 1500 |  |  |  |
|  |  | -trip hazard on access ramp | -plane down |  | 3 |  |  |
|  |  | -smoke stack full of garbage | -clean and cover with >30º hood | 100 | 8 |  |  |
|  |  | -pinch points on suspended bridge | -cover or immobilize | 50 | 3 |  |  |
| PLG05SRW4599P |  | -head entrapment in ladder | in-fill |  |  |  |  |
| con’t |  | -access barrier & 15” opening at ladder | -install | 50 | 3 |  |  |
|  |  | -finger entrapment at bridge barriers | -screw down | 10 | 3 |  |  |
|  |  | -warped platform board | -replace | 10 | 1 |  |  |
|  |  | -play surface on roof | -change to >30º | 500 | 12 |  |  |
|  |  | -steering wheel pinch points | -replace | 60 | 1 |  |  |
|  |  | -ships hull nailed | -screw down | 30 | 4 |  |  |
|  |  | -log chain climber | -pinch points - reset | 50 | 4 |  |  |
|  |  | -entrapment at spiral tube slide | -in fill | 10 | 2 |  |  |
|  |  | -chain climber & ladders | -change to rungs | 100 | 6 |  |  |
| PLG04SPR4599P |  | -entrapment | -in fill | 20 | 2 |  |  |
| Spring Stand |  |  |  |  |  |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  |  | -base material |  |  | 1800 |  |
|  |  |  | -excavate |  | 8 | 2000 |  |
| Total |  |  |  | 3072 | 116 | 3800 |  |

File Name: K:\PLAY\NORTH\WARD-10\WILLOWDL