SITE SPECIFIC RECOMMENDATIONS

SOUTH REGION:	Central District

LOCATION		Woodbine Beach														Ward 26

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -remove one seat, adjust spacing |  | 2 |  |  |
| 3 Belt |  | -tree in 2Y zone | -relocate swings | 25 | 20 |  |  |
| PLG02SSM |  | -improper spacing | -remove one, adjust spacing |  | 2 |  |  |
| 3 Belt |  | -branches in 2Y zone | -prune branches |  | 2 |  |  |
| PLG03SSM |  | -improper spacing | -remove two seats, adjust spacing |  | 2 |  |  |
| 4 Baby |  |  |  |  |  |  |  |
| PLG04TTM |  | -entrapment in handles | -replace handles | 300 | 4 |  |  |
| Spring Teeter Totter |  |  |  |  |  |  |  |
| PLG05TTM |  | -entrapment between handle & seat | -relocate handle |  | 3 |  |  |
| Double Spring Teeter |  |  |  |  |  |  |  |
| PLG06SPR |  | -nil |  |  |  |  |  |
| Spring Motorcycle |  |  |  |  |  |  |  |
| PLG07SPR |  | -nil |  |  |  |  |  |
| Spring Barber Pole |  |  |  |  |  |  |  |
| PLG08SSP |  | -entrapment in handrail | -replace slide | 3500 | 12 |  |  |
| Spiral Slide |  | -entanglement around post |  |  |  |  |  |
| PLG09SST |  | -entrapment | -remove and replace | 2000 | 10 |  |  |
| Straight Slide (purple) |  | -entanglement |  |  |  |  |  |
| PLG10SST |  | -entanglement | -caulk gap | 10 | 1 |  |  |
| Straight Slide (red) |  |  |  |  |  |  |  |
| PLG11SST |  | -entanglement | -caulk gap | 10 | 1 |  |  |
| Straight Slide (green) |  | -water holes at exit | -drill holes |  | 1 |  |  |
| PLG12INM |  | -entanglement at slide | -caulk gap |  | 1 |  |  |
| Hill & Dale |  |  |  |  |  |  |  |
| PLG13CLM |  | -nil |  |  |  |  |  |
| Space Climber |  |  |  |  |  |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
| TOTAL COST |  |  |  | 5845 | 69 | 0 |  |

File Name: K:\SOUTH\WARD-26\WOODBINE.WPD