SITE SPECIFIC RECOMMENDATIONS

SOUTH REGION:	Central District

LOCATION		Chelsea															Ward 21

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -remove two seats & adjust spacing |  | 4 |  |  |
| 3 Baby, 3 Belt |  | -non sufficient zone | -re-install swing to face e/w | 50 | 20 |  |  |
|  |  | -bench in non-encroachment zone | -relocate | 100 | 12 |  |  |
| PLG02SST |  | -entanglement at top | -weld gap | 20 | 2 |  |  |
| Jr. Str. Slide |  | -entrapment under barrier | -weld 2 (22” x 5”) | 20 | 4 |  |  |
| PLG03SPR |  | -nil |  |  |  |  |  |
| Bird Spring Toy |  |  |  |  |  |  |  |
| PLG04SPR |  | -protruding metal handles & footrest | -remove & replace | 1200 | 4 |  |  |
| Horse Spring Toy |  |  |  |  |  |  |  |
| PLG05JRM |  | -barrier panels are <2” | -replace two | 500 | 4 |  |  |
| Jr. Cr. Structure |  | -4 X 4 posts have no caps | -install 4 caps | 50 | 4 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
| TOTAL COST |  |  |  | 1940 | 62 | 0 |  |

File Name: K:\SOUTH\WARD-21\CHELSEA.WPD