SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	Central District

LOCATION		Eastview															Ward 16

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 109 |  | -improper spacing | -remove one, adjust spacing |  | 1 |  |  |
| 6 Baby |  | -chipped paint | -repaint | 50 | 2 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -hanger bearings | -replace | 200 | 3 |  |  |
| PLG02SSM - 109 |  | -improper spacing | -remove two, adjust spacing |  | 1 |  |  |
| Swing Set |  | -chipped paint | -repaint | 50 | 2 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
| PLG03SST - 109 |  | -barriers | -picket | 300 | 4 |  |  |
| Str.Slide |  | -slide side | -modify to 4” | 500 | 4 |  |  |
|  |  | -entanglement | -weld | 50 | 2 |  |  |
|  |  | -chipped paint | -repaint | 30 | 1 |  |  |
| PLG04TTM - 109 |  | -improper spacing | -remove two |  | 2 |  |  |
| Quad Teeter Totter |  | -chipped paint | -repaint | 50 | 2 |  |  |
|  |  | -cushions | -add rubber to bottom of seats | 100 | 3 |  |  |
| PLG05SRM - 109 |  | -entrapment | -add barriers | 100 | 3 |  |  |
| Sr. Cr. Structure |  | -entanglement | -weld | 50 | 2 |  |  |
|  |  | -tire swing | -remove |  | 4 |  |  |
|  |  | -improper access / egress | -remove two panels |  | 2 |  |  |
| PLG05SRM - 109 |  | -barriers | -pickets over 48” | 500 | 8 |  |  |
| con’t |  | improper spacing | -remove hand to hand climber |  | 4 |  |  |
| Base Material |  | -non sufficient | -rototill, add base material 80T |  | 16 | 1200 |  |
|  |  |  | -excavate |  | 8 | 2000 |  |
| Total Cost |  |  |  | 2000 | 76 | 3200 |  |

File Name: K:\SCARB\WARD-16\EASTVIEW.WPD