SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	North District

LOCATION		Highland Heights														Ward 17

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 077 |  | -improper baby seats | -replace | 240 | 1 |  |  |
| 4 Baby |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -chipped | -repaint | 50 | 2 |  |  |
| PLG02SSM - 077 |  | -improper spacing | -remove three, adjust spacing |  | 1 |  |  |
| 6 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -chipped | -repaint | 50 | 2 |  |  |
| PLG03SST - 077 |  | -entrapment | -add backing to stairs | 200 | 2 |  |  |
| Jr. Straight Slide |  | -entanglement | -weld or caulk | 10 | 1 |  |  |
|  |  | -platform | -extend to 22” | 300 | 3 |  |  |
|  |  | -barriers | -add pickets >30” | 200 | 3 |  |  |
| PLG04SSP - 077 |  | -platform | -extend to 22” | 300 | 3 |  |  |
| Sr. Spiral Slide |  | -exit | -add 12” < 5º | 400 | 3 |  |  |
|  |  | -barriers | -add pickets & rails | 400 | 4 |  |  |
| PLG05FPM - 077 |  | -improper access | -add stairs | 1000 | 4 |  |  |
| Fireman Pole |  | -barriers | -add pickets | 300 | 3 |  |  |
|  |  | -pole height | -extend to 60” above platform | 100 | 2 |  |  |
|  |  | -chipped | -repaint | 50 | 2 |  |  |
| PLG06TCM - 077 |  | -entrapment | -add pickets, modify rails | 40 | 3 |  |  |
| Tank Climber |  | -entanglement | -weld skirt | 50 | 3 |  |  |
| PLG07GCM - 077 |  | -chipped | -repaint | 50 | 2 |  |  |
| Globe Climber |  |  |  |  |  |  |  |
| PLG08SRM - 077 |  | -improper play space | -cap supports | 150 | 3 |  |  |
| Sr. Cr. Structure |  | -tire swing | -remove swing & support |  | 6 |  |  |
|  |  | -barriers | -add pickets | 300 | 4 |  |  |
|  |  | -fireman pole | -relocate | 100 | 2 |  |  |
| Base Material |  | -compacted | -rototill, add base material 66T |  | 8 | 990 |  |
|  |  | -non sufficient safety zone | -excavate |  | 8 | 1500 |  |
| Total Cost |  |  |  | 4310 | 77 | 2490 |  |

File Name: K:\PLAY\SCARB\WARD-17\HIGHLAND.WPD