SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	West District

LOCATION	 	Islington Park														Ward 6

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG0101SSW1546P |  | -improper spacing on baby swing | -remove one swing & adjust |  | 8 |  |  |
| 3 Baby 2 Belt 1 Tire |  | -tire swing not up to standard | -remove tire, replace with belt | 100 | 2 |  |  |
|  |  | -play surface on top frame | -install wood and caps | 400 | 2 |  |  |
| PLG0201TTW1546P |  | -not up to standard | -remove |  | 4 |  |  |
| Teeter Totter |  |  |  |  |  |  |  |
| PLG0301JRW1546P |  | -barriers slides | -install barriers | 200 | 4 |  |  |
| Jr. Cr. Structure |  | -play surface on top rails | -install 1" strip | 300 | 2 |  |  |
|  |  | -trip hazard at entrances | -remove 2X4 |  | 1 |  |  |
|  |  | -entrapment at slide frames | -install plastic | 100 | 2 |  |  |
|  |  | -no assist handles | -install handles near ladders | 100 | 2 |  |  |
| PLG0401SRW1546P |  | -rope missing on climber | -replace | 50 | 1 |  |  |
| Sr. Cr. Structure |  | -hand to hand climber | -refit to level | 250 | 6 |  |  |
|  |  | -play surface on top rails | -install 1" strip | 300 | 2 |  |  |
|  |  | -log chain climber | -change to rungs | 100 | 4 |  |  |
|  |  | -4X4 vertical ladder | -change to rungs | 100 | 2 |  |  |
|  |  | -pinch points suspension bridge | -immobilize | 50 | 4 |  |  |
|  |  | -trip hazard at entrances | -remove 2X4 |  | 1 |  |  |
| Base Material |  | -compacted | -rototill, add base 80T |  | 8 | 1200 |  |
|  |  |  | -excavate |  | 8 | 1500 |  |
|  |  |  |  | 2050 | 63 | 2700 |  |

File Name: K:\PLAY\NORTH\WARD-6\ISLINGTN