SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	North District

LOCATION		L’Amoreaux North		 												Ward 17

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 096 |  | -improper spacing | -remove two, adjust spacing |  | 1 |  |  |
| 4 Baby |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -improper baby seats | -replace | 120 | 1 |  |  |
| PLG02SSM - 096 |  | -improper spacing | -remove two, adjust spacing |  | 1 |  |  |
| 6 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
| PLG03TTM - 096 |  | -cushioning | -add rubber to bottom of seats | 150 | 3 |  |  |
| Teeter Totter Quad |  | -improper spacing | -remove two, adjust |  | 2 |  |  |
| PLG04SST - 096 |  | -entrapment | -remove, replace with straight slide | 2000 | 8 |  |  |
| Birdcage Str. Slide |  | -entanglement |  |  |  |  |  |
| PLG05SRM - 096 |  | -not up to standard | -remove, replace with jr.str. Slide | 1500 | 8 |  |  |
| Sr. Cr. Structure |  |  |  |  |  |  |  |
| PLG06CLM - 096 |  | -non sufficient safety zone | -excavate |  |  |  |  |
| Globe Climber |  |  |  |  |  |  |  |
| PLG07SPR - 096 |  | -non sufficient safety sone |  |  |  |  |  |
| Turtle Spring Toy |  |  |  |  |  |  |  |
| PLG08SPR - 096 |  | -non sufficient safety zone |  |  |  |  |  |
| Whale Spring Toy |  |  |  |  |  |  |  |
| PLG09SPR - 096 |  | -non sufficient safety zone |  |  |  |  |  |
| Horse Spring Toy |  |  |  |  |  |  |  |
| PLG10CLM - 096 |  | -slide width | -add middle | 200 | 3 |  |  |
| Billy Goat Climber |  | -slide side | -add 4” sides | 400 | 5 |  |  |
|  |  | -barriers | -add egress/access | 200 | 3 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  | -non sufficient safety zone | -add base material 55T |  | 8 | 825 |  |
|  |  |  | -excavate |  |  | 1000 |  |
| Total Cost |  |  |  | 4590 | 53 | 1825 |  |

File Name: K:\PLAY\SCARB\WARD-17\LAMOR-N.WPD