SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	East District

LOCATION 		Maxome Park															Ward 10

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSW4559P |  | -tire swing | -remove tire swing and one beam |  |  |  | -site redevelopment due |
| 3 Baby 2 Belt 1 Tire |  | -baby swing | -remove one baby swing and adjust |  |  |  | to lack of base material |
|  |  | -play surface | -add 2X2 |  |  |  | and equipment |
| PLG02TTW4559P |  | -pinch / crush hazard | -remove |  |  |  |  |
| Teeter Totter |  |  |  |  |  |  |  |
| PLG03JRW4559P |  | -barriers >30” | -picket with proper egress/access |  |  |  |  |
| Jr. Cr. Structure |  | -improper play surface | -remove surfaces >2” replace <2” |  |  |  |  |
|  |  | -tires no holes | -drill |  |  |  |  |
|  |  | -4 X4 log chain too wide | -change to rungs |  |  |  |  |
|  |  | -no side enclosures on slide | -T.B.D. |  |  |  |  |
|  |  | -neck entrapment on slide supports | -in fill |  |  |  |  |
| PLG04SRW4559 |  | -barriers >48” | -pickets with proper egress/access |  |  |  |  |
| Sr. Cr. Structure |  | -improper play surface | -remove surfaces >2” replace <2” |  |  |  |  |
|  |  | -track ride does not meet standard 14.5 | -remove or relocate |  |  |  |  |
|  |  | -rope climber fastener | -change fasteners |  |  |  |  |
|  |  | -log climbers too large / not steep enough | -modify angle & rungs |  |  |  |  |
|  |  | -balance beam too high | -lower |  |  |  |  |
|  |  | -suspension bridge has pinch points | -immobilize |  |  |  |  |
|  |  | -horizontal ladder | -modify |  |  |  |  |
|  |  | -rung ladder <75º | -make 75 - 90º |  |  |  |  |
|  |  | -neck entrapment | -in-fill |  |  |  |  |
| Base Material |  | -compacted | -rototill |  |  |  |  |
|  |  |  | -add base 440 T |  |  |  |  |
|  |  |  | -excavate |  |  |  |  |
| Total |  |  |  | 0 | 0 | 0 |  |

File Name: K:\PLAY\NORTH\WARD-10\MAXOME