SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	South District

LOCATION		Stamford															Ward 13

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 037 |  | -improper spacing | -remove one, adjust spacing |  | 1 |  |  |
| 6 Baby |  | -improper seats | -replace two | 120 | 1 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -chipped paint | -repaint | 50 | 2 |  |  |
| PLG02SSM - 037 |  | -improper spacing | -remove two, adjust spacing |  | 1 |  |  |
| Swing Set |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -chipped paint | -repaint | 50 | 2 |  |  |
| PLG03SST - 037 |  | -entanglement | -weld | 50 | 2 |  |  |
| Jr. Str. Slide |  | -entrapment | -stair backing | 100 | 2 |  |  |
|  |  | -barriers | -add pickets > 30” | 200 | 3 |  |  |
|  |  | -chipped paint | -repaint | 50 | 2 |  |  |
| PLG04SST - 037 |  | -entanglement | -weld | 50 | 2 |  |  |
| Sr. Str. Slide |  | -entrapment | -stair backing | 100 | 2 |  |  |
|  |  | -barrier | -add picket > 48” | 200 | 2 |  |  |
|  |  | -slide side | -modify to 4” | 400 | 4 |  |  |
|  |  | -chipped paint | -repaint | 50 | 2 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  | -non sufficient safety zone | -excavate |  |  | 1000 |  |
|  |  |  | -add base material 33T |  | 16 | 495 |  |
| Total Cost |  |  |  | 1440 | 54 | 1495 |  |

File Name: K:\SCARB\WARD-13\STAMFORD.WPD