SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	East District

LOCATION 		Talwood Park														Ward 11

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM5583P |  | -none |  |  |  |  |  |
| 2 Baby Swing Set |  |  |  |  |  |  |  |
| PLG02SSM5583P |  | - safety zone overlaps | - relocate | 100 | 10 |  |  |
| 2 Belt Swing Set |  |  |  |  |  |  |  |
| PLG03SSM5583P |  | -none |  |  |  |  |  |
| 2 Belt Swing Set |  |  |  |  |  |  |  |
| PLG08SRW5583P |  | -fireman pole platform to top is 57” and too close to platform | -retrofit | 100 | 2 |  | -remove 8 dead trees |
| Sr. Cr .Structure |  | - entanglement points | -infill | 100 | 4 |  |  |
|  |  | -no alternate and support at top of rope climbing wall, | -find alternative or remove & barrier | 50 | 3 |  |  |
|  |  | -bottom unattached step is unsafe | -remove, add proper step & support | 300 | 8 |  |  |
|  |  | -elevated play surface | -rout wood, cover steel at climber |  | 3 |  |  |
| PLG05SPR5583P |  | -no foot rest | -correct |  |  |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG065SPR5583P |  | -possible entrapment | -in fill | 20 | 1 |  |  |
| Spring Toy Standing |  |  |  |  |  |  |  |
| PLG04CCW5583P |  | -entanglement points all over | - remove or replace or in-fill | 100 | 3 |  |  |
| Wall Climber |  |  |  |  |  |  |  |
| PLG07SBW5583P |  | -shear points | -remove lower red section | 20 | 1 |  |  |
| Sand Box |  | -does not meet standards | -immobilize |  |  |  |  |
|  |  | -encroaches on standing spring toy | -relocate | 20 | 2 |  |  |
| Base Material |  | -compacted | -rototill and top up 80T |  | 8 | 1200 |  |
|  |  |  | -excavate |  | 8 | 1500 |  |
| Total |  |  |  | 810 | 53 | 2700 |  |

File Name: K:\PLAY\NORTH\WARD-11\TALWOOD