SITE SPECIFIC RECOMMENDATIONS

SOUTH REGION:	West District

LOCATION		Wanless															Ward 22

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -remove one seat, adjust spacing |  |  |  | site replacement and |
| 3 Belt |  |  |  |  |  |  | consolidation |
| PLG02SSM |  | -improper spacing | -remove three seats, adjust spacing |  |  |  |  |
| 3 Belt, 3 Baby |  |  |  |  |  |  |  |
| PLG03TTM |  | -entrapment in handles | -replace handles |  |  |  |  |
| Teeter Totter |  |  |  |  |  |  |  |
| PLG04SPR |  | -nil |  |  |  |  |  |
| Spring Barber |  |  |  |  |  |  |  |
| PLG05CLM |  | -nil |  |  |  |  |  |
| Climber |  |  |  |  |  |  |  |
| PLG06SST |  | -entrapment in ladder & rails | -remove structure |  |  |  |  |
| Sr. Straight Slide |  | -entanglement in entrance |  |  |  |  |  |
|  |  | -no sitting section |  |  |  |  |  |
| PLG07SST |  | -entrapment | -remove structure |  |  |  |  |
| Sr. Straight Slide |  | -entanglement |  |  |  |  |  |
|  |  | -no sitting area |  |  |  |  |  |
| PLG08SST |  | -nil |  |  |  |  |  |
| Sr. Straight Slide |  |  |  |  |  |  |  |
| PLG09PIP |  | -no rail | -remove |  |  |  |  |
| Crawl Pipe |  | -no play surface |  |  |  |  |  |
| PLG10SPR |  | -nil |  |  |  |  |  |
| Spring Tractor |  |  |  |  |  |  |  |
| PLG11INM |  | -transition zone | -picket 4’ |  |  |  | replace structure $8,000 |
| Sr. Cr. Structure |  | -no barriers | -picket 80’ |  |  |  |  |
|  |  | -entrapment in crawl tube | -close with plastic |  |  |  |  |
|  |  | -entrapment in crawl tube platform | -close with plastic |  |  |  |  |
|  |  | -improper exit on tube slide | -retro fit with new exit |  |  |  |  |
|  |  | -entrapment at tube slide supports | -fill with plastic |  |  |  |  |
|  |  | -straight slide has no exit | -remove |  |  |  |  |
|  |  | -open steering wheel | -replace with solid |  |  |  |  |
|  |  | -vertical crawl tube entrapment | -remove |  |  |  |  |
|  |  | -entrapment between platform | -fill with 2X6 24’ |  |  |  |  |
| Base Material |  | -compacted | -rototill |  |  |  |  |
| TOTAL COST |  |  |  | 0 | 0 | 0 |  |

File Name: K:\PLAY\SOUTH\WARD-22\WANLESS.WPD